## Slide 1: Review of Angle Lake Station Area Implementing Regulations
SeaTac Planning Commission
March 15, 2016

## Slide 2
Meeting Overview
Review:
  The AL District Plan: Parking
  Meeting with Wright Runstad overview
  AL policy direction
  What does the code currently require
  Staff recommendations to address these issues
  Planning Commission input is sought with regard to the proposed recommendations/staff direction.

## Slide 3
Zoning Code Framework
Use Charts – what’s permitted and where?
Urban Design
Circulation & Connectivity
On site Open Space
Site Planning
Parking
Building Design
Landscaping

## Slide 4
Vision & Objective
AL Plan Vision: create a pedestrian oriented transit community and a District Center as a focal point
Urban Design Objective: to promote high quality building and streetscape design

## Slide 5
How will this vision be achieved?
Human scale buildings
Engage with sidewalk
Create consistent street wall
Minimize impact of parking
Safe & convenient sidewalks
CPTED prioritized
The ‘right’ uses that support activity, employment and housing

## Slide 6
Location of Parking
AL Policy Guidance:
• Continue to require parking to the side and back of buildings in the District.
Existing Standards:
No parking in front of a building (including corner lots)
Parking allowed to the side of the building
1 double loaded drive aisle permitted for first 40’ (CC)
Landscape island for every 7 stalls
Staff Recommendation:
No parking in front of the building (including corner lots)
Parking allowed to side of building, setback min 20’ from ROW and landscaped
Remove requirement for landscape island for every 7 stalls

## Slide 7
Parking Lot Screening
AL Policy Guidance
Ensure parking lots adjacent to street frontages and sidewalks are sufficiently landscaped.
Existing Standards:
1 parking island per 7 stalls
10’ of street frontage landscaping required (50% can be placed elsewhere onsite)
Staff Recommendation:
Remove requirement for landscape island
Parking to be setback one parking length (20’) from front property line and landscaped

## Slide 8
Driveway Cuts
AL Policy Guidance
Consider regulations that limit the maximum number of curb cuts per site
Existing Standards:
Joint use of driveways is encouraged
1 driveway per 150’ of street frontage along arterials (100’ elsewhere)
Staff Recommendation:
No change to existing standards

## Slide 9
Parking Reductions
AL Policy Guidance:
Evaluate the appropriate parking for projects in close proximity to transit facilities or that provide shared parking between uses including consideration of: - Reduction of parking requirements - Establishment of maximum parking standards. - Shared parking reductions
Existing Standards:
Shared parking may be approved by Director. Max 10% reduction of each use
Up to 35% reduction if located within “regularly scheduled high capacity transit”
Staff Recommendation:
No change to existing standards
Establish a maximum parking standard. Staff currently reviewing

## Slide 10
Bicycle Parking
AL Policy Guidance
Amend the Zoning Code to include provisions for bicycle parking and storage as part of new developments
Existing Standards:
Must be within a structure and secure from general public
154th: bicycle parking at 1 space per 10 parking spaces
Staff Recommendation:
No change to existing standards and adopt 154th standard for bicycle parking.
Bicycle parking can be provided as racks and/or lockers

## Slide 11
Residential Parking
AL Policy Guidance
Evaluate the appropriate parking standards for residential projects including consideration of: - Allowing off-site parking that meets certain locational
criteria - Tandem stalls for residential uses
Existing Standards:
Shared parking may be approved by Director. Max 10% reduction of each use
Tandem stalls permitted with a garage and for 50% of units
Staff Recommendation:
A study conducted by right size parking recommended no reduction to SeaTac MF parking requirements
Staff currently reviewing maximum parking requirements
No change to tandem parking

## Slide 12
Meeting with Wright Runstad
Met to discuss development objectives and ‘truth test’ some proposed standards
Recommended the following:
Transparency requirements – 75%-80% of street frontage
Open space at 5% is standard
Require commercial space be constructed ground floor but do not require retail uses
Minimum floor to floor height: 14’ (steel) and 12’ (concrete)
Place making very important
Flexibility to construct on street parking
Reduce parking near transit if want to promote transit
Do not require wedding cake construction
8’ sidewalks (4’sidewalk+4’ landscaping) is absolute minimum

## Slide 13
END OF PRESENTATION